Physics 112: Laws and Concepts summary

23-Coulomb’s Law:

Find the modulus of the force magnitude. Then find the direction by knowing whether charges attract or repel. Force is a vector; remember always to specify its direction.

For charge distribution, use the key equation, search for symmetry or one of the three notations:

| The key equation for all the uniform or non-uniform charge distribution |  |
| --- | --- |

Special cases!

Motion of charges in electric fields:

24-Gauss’s Law:

Remember the difference between the TOTAL FLUX and FLUX of an Area:  Flux of an area A

Total Flux over the whole volume.

Gauss’s Law

| Infinite line of charges |  |
| --- | --- |
| Infinite non conducting sheet |  |
| Inside a conductor | zero |
| Outside a spherical conductor |  |
| Inside an Insulating sphere r < R |  |
| Outside an Insulating sphere r > R |  |

25-Electric Potential:

POTENTIAL IS NOT A VECTOR

The Potential inside a spherical shell equals a constant

Potential Energy difference between 2 points and potential difference.

26-Capacitance:

Q=CV

Capacitance for parallel plates only. Kd is the dielectric constant, for air it is 1.

To find the capacitance, calculate the potential difference between the two points in the insulator, and then divide by the charge.

Rewiring of capacitors, search for the constant Q C V.

CASE#1: Capacitor disconnected, and a dielectric was inserted. ( Q Constant)

CASE#2: Capacitor connected to a battery, dielectric inserted ( V Constant) Q=Q0K

Parallel Capacitors: Cequivalent=C1+C2+C3+…… (They have equal potential difference)

Series Capacitors : Cequivalent = 1/C1 + 1/C2 + 1/C3 +………  (They have equal charge)

Energy stored in a capacitor.

27-Resistance:

|  | n: number of charges per unit volume |
| --- | --- |
|  | : T0=20(C |

28-DC Circuits:

| Series resistors | Parallel resistors |
| --- | --- |

You are aware of the Whetstone bridge case (Ratio concept) (

If the current was going to pas in either a zero resistance, and any other resistance, it will select the zero resistance. (

Kirchhoff’s method of solving circuits:

1-Draw a NEAT DIAGRAM in your paper.

2-Assume paths of current entering and leaving a certain node point: I1+I2=I

3-Put the signs on the resistors and batteries (How?)

You know that the current moves from high to low potential. Then for resistor current goes from down to up..hence the lower end has positive sign, and the upper end takes the negative sign.

4-Form your equations to get the 3 unknowns (I1,I2,I) by moving in one cycle till its end

For the RC circuit, at charge t=0, the capacitor is thirsty for charges: hence it will withdraw all the charges inside till it gets satisfied. When it is full, it does not accept currents to pass in (open circuit)

: Equation of current growth and decay

:Equation of charge growth

charge decay equation

wheretime constant

Chapter 29:

: Force on a charge trapped in a magnetic field.

:       :    :

: Force on a current carrying wire in B.

Velocity selector:       :

Mass spectrometer: :       :

Cyclotron:

Lorentz Equation:

Hall effect: :  Hall effect

Fleming left hand rule: finding the direction of the force acting on a current carrying wire in a magnetic field: It is your left hand, the one that you do not eat with (

Chapter 30:

BIOTSAVART: JUST FOR YOUR KNOWLEDGE:

| Magnetic Field due to infinite wire ( d>R) |  |
| --- | --- |
| Magnetic Field due to a loop | at its center: else leave the exam! |
| Magnetic Field due to a toroid | at its center |
| Magnetic Field of finite wire |  |
| Magnetic Field of arc of a loop |  |
| Magnetic field of Solenoid |  |
| Magnetic field due to a wire ( r <R ) |  |
| Ampere’s Law: | Magnetic flux: |
| Ampere’s Maxwell’s equation: Displacement current |
| Displacement Current: |

Chapter 31:

| Faraday’s Law: | Motional EMF: |
| --- | --- |

Chapter 32:

Induction:

Inductance:

Chapter 33:

:

Negative means that volt leads the current

:

| Phase angle: | Impedance: |
| --- | --- |
| Power: |

Prepared by: Moataz M. Attallah (mizoa@aucegypt.edu) http://come.to/fiqi